## Slide 1: Duckietown Presentation
Tobias, Manjunath, Yifan

## Slide 2: Autonomous Navigation & Real Time Mapping on iOS
System combining both of these things with output to the iOS mobile application
Empower users with a comprehensive understanding of a robot's movements in real-time, even in uncharted territories
Intuitive iOS application that offers both utility and insight into autonomous robotic navigation, as well as key information about the robot itself.
1. Lane Following
2. Trajectory & Analysis
3. iOS Mobile Application

## Slide 3: Midterm: Project Outline
Step 1: Assembly
& Software Setup
Step 2: Calibration
Wheels
Camera
Lane following Duck
Step 3: Project Definition
Lane following Demo
Mobile App with track layout

## Slide 4: Midterm: Project Outline
Step 4: Basic Functionality
Wheel Control
Camera Control
Step 5.2: Lane detection
Step 6.2: Lane following optimization
Step 7: Autonomous mapping System
Step 8:Optimization & error handling
FInal Presentation
Step 5.1: Dynamic mapping system
Step 6.1: Map creation

## Slide 5: AprilTags & Lane Following

## Slide 6: AprilTags
AprilTags are binary markers designed for easy detection and robust identification by computer vision algorithms.
They offer precise localization capabilities, crucial for tasks like navigation, object tracking, and augmented reality applications
Small payload: 4-12 bits of data
Easy detection and robust identification
Long-range detectability

## Slide 7: AprilTag detection
These are detected using Computer vision libraries like OpenCV.
After converting to grey_img we can detect tag using apriltag.detector() in dt-apriltag.
Notes: This array likely contains the image data coming from the camera.

## Slide 8
AprilTag Detection:

## Slide 9
Integrating AprilTags detection and LED lights.
Duckiebot recognising different AprilTags by exhibiting to different colours of LED lights.

## Slide 10: Lane Following
Notes: It plays a crucial role in ensuring safe and efficient transportation, reducing accidents and congestion.

## Slide 11: Implementation
This OpenCV code captures a camera image, converts it to HSV for color filtering, and creates a mask to isolate a yellow color.
After this, we find all the yellow dotted lines used to follow the lane.

## Slide 12: PID Controller
The error equation in the controller:
error=( x + sizeratio × y − goal ) × pixelscale
x = the left most side of the closest dotted line
y = the top of the closest dotted line divided by two
sizeratio = distance from centre of duckiebot to dotted line.This addresses the vanishing point problem.
goal = where the bot wants to be. Represented by a blue vertical line in the image
pixelscale = scales the error down to account for a large error in pixels relative to a small error in angle

## Slide 13: Lane Following

## Slide 14: Trajectory Generation and Analysis

## Slide 15: Trajectory Generation and Analysis
Wheel encoder data to estimate Duckiebot trajectory
Analyse the movement patterns on a track
Primary goal: coordinates of the robot's position
Mapping location on a coordinate system using an “Elementary Trajectory Model for the Differential Steering System”

## Slide 16: Calculation of Coordinates
Theory behind it is pretty simple:
Subscribe to wheel encoders
Calculate the change in values to the previous moment in time
Keep a direction value at each point in time and update it every time encoders change
Calculate the coordinates based on distance traveled per wheel, orientation, wheel distance & wheel radius

## Slide 17
Calculation of Coordinates
Code Snippet

## Slide 18: Calculation of Coordinates Challenges
Things needed to consider:
Encoders are not 100% reliable
The Duckiebot tends to move a bit to the left when supposed to only go straight
Extremly Quick changes might not be as accurate
Because of big challenges in the beginning we tried out Slam, which did not improve the situation

## Slide 19: Midterm Review: Objective: Dynamic mapping system
Real Time perception
  Active perception of driving course
Iterative construction of the map
  Construction of living, dynamic map of Duckietown
  Usage of BFS or DFS traversal to find all “nodes” of the map

## Slide 20: Slam Orb
Midterm Review:
Dynamic Map

## Slide 21: Calculation of Coordinates Output

## Slide 22: Analyzation of Track Types Output
Track Types can be analysed:
  Straights
  Left Curves
  No movement
Posted as a sequence of Tracks that have the Duckiebot travelled

## Slide 23: Analyzation of Track Types How does it work?
How does it work:
Absolute degree of the slope between the start and end coordinates of the track the bot has just crossed
Simulates the direction of movement using the orientation value at the end and start point
Special attention has to be paid here to the calculation of the slope → depends on the orientation value ‘theta’: North sout or west east movement

## Slide 24
Code Snippet

## Slide 25: Simulation of the Track
Simulation of the Track just passed using Bezier Curve and Linear Modelling
Defines the track the bot drived on

## Slide 26: Simulation of the Track

## Slide 27
Simulation in action

## Slide 28: Visualization
Visualisation either in Map_Maker Script in Project or on iOS
Publisher in the Trajectory class publishes a message as a string containing the trajectory coordinates and the simulated trajectory coordinates every time the run method runs (at a frequency of 20Hz).

## Slide 29
Visualisation of Trajectory in real time

## Slide 30: iOS Application

## Slide 31: Mobile ROS - an iOS application for robots
Device status fetching
all information in one
customizable
expandable to other application (explain later)

## Slide 32: Mobile ROS - an iOS application for robots

## Slide 33: Mobile ROS - an iOS application for robots
Control with your mobile
force sensing
subtle control
easy to use

## Slide 34
iOS Mobile Application in action

## Slide 35: Demo Video 1
Basic Track: https://youtu.be/SlGvRx_gKrY

## Slide 36: Demo Video 2
Advanced Track: https://youtu.be/PKKq_eWwhZE

## Slide 37: Demo Video 3
End-Level Track https://youtu.be/yZKdoTJIhHA

## Slide 38: Thank you

## Slide 39: Bibliography
Works Cited
“Beginner - Code Hierarchy — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/code-hierarchy/index.html. Accessed 13 Mar. 2024. priority_high Webpage author
priority_high Date published
“Bezier.curve Module — Bezier 2023.7.28 Documentation.” Bezier.readthedocs.io, bezier.readthedocs.io/en/stable/python/reference/bezier.curve.html. Accessed 13 Mar. 2024. priority_high Webpage author
priority_high Date published
“Exercise 3.” Ekhumbata.github.io, ekhumbata.github.io/Adventures-in-Duckietown/exercise3.html. Accessed 14 Mar. 2024. priority_high Webpage author
priority_high Date published
“Golnaz Mesbahi - Lab 3.” Github.io, 2023, golnazmes.github.io/Lab%203.html. Accessed 14 Mar. 2024. priority_high Webpage author
“How to Generate Random Points in a Line.” De.mathworks.com, de.mathworks.com/matlabcentral/answers/175107-how-to-generate-random-points-in-a-line?s_tid=prof_contriblnk. Accessed 13 Mar. 2024. priority_high Webpage author
priority_high Date published
“Isarlab-Department-Engineering/Ros_dt_lane_follower.” GitHub, 21 Nov. 2023, github.com/isarlab-department-engineering/ros_dt_lane_follower. Accessed 14 Mar. 2024. priority_high Webpage author
“Lane Following Robot Using OpenCV.” Hackster.io, www.hackster.io/Aasai/lane-following-robot-using-opencv-da3d45. priority_high Webpage author
priority_high Date published
Mazur, Izabela, and Kim Moshenko. “3.4 Understand Slope of a Line – Optional.” Opentextbc.ca, 8 Sept. 2021, opentextbc.ca/businesstechnicalmath/chapter/understand-slope-of-a-line-2/. Accessed 13 Mar. 2024. priority_high Volume number
priority_high Issue number
“New ROS DTProject — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/ros/create-project.html. Accessed 12 Mar. 2024. priority_high Webpage author
priority_high Date published
Project , Rossum. “A Tutorial and Elementary Trajectory Model for the Differential Steering System.” Rossum.sourceforge.net, rossum.sourceforge.net/papers/DiffSteer/. priority_high Date published
“Publish Chassis-Level Commands — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/ros/twist-control.html. Accessed 13 Mar. 2024. priority_high Webpage author
priority_high Date published
“Publish to Wheels — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/ros/wheel-control.html. Accessed 13 Mar. 2024. priority_high Webpage author
priority_high Date published
Rosebrock, Adrian. “AprilTag with Python.” PyImageSearch, 2 Nov. 2020, pyimagesearch.com/2020/11/02/apriltag-with-python/.
Samiei, Mandana. “Mandanasmi/Lane-Slam.” GitHub, 3 Feb. 2024, github.com/mandanasmi/lane-slam. Accessed 14 Mar. 2024.
“Subscribe to Wheel Encoders — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/ros/wheel-encoder-reader.html. Accessed 12 Mar. 2024. priority_high Webpage author
priority_high Date published
“What Is Difference between Rospy.spin() and While Not Rospy.is_shutdown()?” The Construct ROS Community, 2 Jan. 2020, get-help.theconstruct.ai/t/what-is-difference-between-rospy-spin-and-while-not-rospy-is-shutdown/1849. Accessed 12 Mar. 2024. priority_high Webpage author
“Beginner - Code Hierarchy — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/code-hierarchy/index.html. Accessed 13 Mar. 2024.
“Bezier.curve Module — Bezier 2023.7.28 Documentation.” Bezier.readthedocs.io, bezier.readthedocs.io/en/stable/python/reference/bezier.curve.html. Accessed 13 Mar. 2024.
“Exercise 3.” Ekhumbata.github.io, ekhumbata.github.io/Adventures-in-Duckietown/exercise3.html. Accessed 14 Mar. 2024.
“Golnaz Mesbahi - Lab 3.” Github.io, 2023, golnazmes.github.io/Lab%203.html. Accessed 14 Mar. 2024.
“How to Generate Random Points in a Line.” De.mathworks.com, de.mathworks.com/matlabcentral/answers/175107-how-to-generate-random-points-in-a-line?s_tid=prof_contriblnk. Accessed 13 Mar. 2024.
“Isarlab-Department-Engineering/Ros_dt_lane_follower.” GitHub, 21 Nov. 2023, github.com/isarlab-department-engineering/ros_dt_lane_follower. Accessed 14 Mar. 2024.
“Lane Following Robot Using OpenCV.” Hackster.io, www.hackster.io/Aasai/lane-following-robot-using-opencv-da3d45.
Mazur, Izabela, and Kim Moshenko. “3.4 Understand Slope of a Line – Optional.” Opentextbc.ca, 8 Sept. 2021, opentextbc.ca/businesstechnicalmath/chapter/understand-slope-of-a-line-2/. Accessed 13 Mar. 2024.
“New ROS DTProject — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/ros/create-project.html. Accessed 12 Mar. 2024.
Project , Rossum. “A Tutorial and Elementary Trajectory Model for the Differential Steering System.” Rossum.sourceforge.net, rossum.sourceforge.net/papers/DiffSteer/.
“Publish Chassis-Level Commands — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/ros/twist-control.html. Accessed 13 Mar. 2024.
“Publish to Wheels — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/ros/wheel-control.html. Accessed 13 Mar. 2024.
Rosebrock, Adrian. “AprilTag with Python.” PyImageSearch, 2 Nov. 2020, pyimagesearch.com/2020/11/02/apriltag-with-python/.
Samiei, Mandana. “Mandanasmi/Lane-Slam.” GitHub, 3 Feb. 2024, github.com/mandanasmi/lane-slam. Accessed 14 Mar. 2024.
“Subscribe to Wheel Encoders — Book-Devmanual-Software - Daffy.” Docs.duckietown.com, docs.duckietown.com/daffy/devmanual-software/beginner/ros/wheel-encoder-reader.html. Accessed 12 Mar. 2024.
“What Is Difference between Rospy.spin() and While Not Rospy.is_shutdown()?” The Construct ROS Community, 2 Jan. 2020, get-help.theconstruct.ai/t/what-is-difference-between-rospy-spin-and-while-not-rospy-is-shutdown/1849. Accessed 12 Mar. 2024.